## Slide 1
INTERNSHIP PROJECT
IoT-Based Industrial Machine Monitoring and Cable Fault Visualization Using ESP8266
Embedded Systems Engineering · ESP8266 NodeMCU Platform

## Slide 2
PROJECT OVERVIEW
Problem Statement & Objectives
The Challenge
Industrial machines operate without real-time temperature or vibration monitoring, leading to undetected failures
Cable faults in industrial electrical systems are difficult to identify and monitor in real time
Manual inspection is slow, costly, and unsafe
Project Objectives
Monitor machine health parameters continuously via IoT sensors
Detect and display cable fault levels in real time
Deliver a live web dashboard with remote alarm acknowledgment

## Slide 3
COMPONENTS
Hardware & Software Stack
Hardware
ESP8266 NodeMCU
Wi-Fi enabled microcontroller — core processing unit
DHT11 Sensor
Temperature & humidity monitoring
SW-420 Vibration Sensor
Machine vibration anomaly detection
Potentiometer + Push Button + Buzzer
Cable fault simulation, alarm acknowledgment, and alert output
Software
Arduino IDE
Firmware development & serial upload
ESP8266 Web Server
Embedded HTTP server for live data streaming
HTML / CSS Dashboard
Responsive browser-based monitoring interface

## Slide 4
ARCHITECTURE
System Architecture
Alarm & Buzzer
Web Dashboard
ESP8266
Sensors
All sensor data is aggregated by the ESP8266, transmitted over Wi-Fi, and rendered on a local web dashboard. Threshold breaches trigger an audible alarm, acknowledged via push button.

## Slide 5
WORKING PRINCIPLE
How the System Operates
Temperature Monitoring
DHT11 samples ambient and machine temperature at fixed intervals, transmitted live to dashboard
Vibration Detection
SW-420 detects abnormal mechanical vibration; threshold breach flags machine anomaly
Cable Fault Visualization
Potentiometer simulates different cable fault conditions, and the ESP8266 visualizes the corresponding fault level on the web dashboard.
Live Web Dashboard
Built-in web server hosts HTML/CSS interface — accessible from any browser on the network
Alarm Acknowledge
Buzzer triggers on fault; push button silences alarm and logs acknowledgment event

## Slide 6
RESULTS
Dashboard Output & System Performance
Live Monitoring Parameters
🌡️ Temperature
Real-time DHT11 readings displayed in °C with threshold alert
⚡ Cable Fault Visualization
Fault severity indicator based on potentiometer input simulation
〰️ Vibration Status
Normal / Anomaly state from SW-420 sensor output
🔔 Alarm Status
Active / Acknowledged state with push-button reset confirmation
Dashboard Screenshots

## Slide 7
CONCLUSION
Key Takeaways & Future Scope
Advantages
Low-cost, scalable IoT architecture using ESP8266
Real-time remote monitoring without dedicated infrastructure
Immediate fault alerts with acknowledgment workflow
Industrial Applications
Manufacturing floor machine health monitoring
Industrial electrical distribution monitoring
Smart factory predictive maintenance systems
Future Scope
Integrate cloud platforms (AWS IoT / Blynk) for remote access beyond LAN
Add machine learning for predictive fault analysis
Expand sensor array: current, voltage, and acoustic sensors
Deploy GSM/LTE module for offline industrial environments

## Slide 8
THANK YOU!
Thank you for your valuable time.